## Slide 1
SiL, HiL testing plan for Year 2

## Slide 2
Verification and Validation process
MiL & SiL
Functional Requirements
Processor in Loop (PiL)
HiL

## Slide 3
Hardware in the loop setup 1
Planning and Control
Raw Control actions
Vehicle Dynamics Model
CAN Interface
Digital Twin
dSPACE Vehicle Dynamics Models

## Slide 4
Using the information on the tire-road friction coefficient, vehicle and traffic data and vehicle configuration, it is determined whether a safe lane change is possible.
Xiangkun He, Yulong Liu, Chen Lv, Xuewu Ji & Yahui Liu (2019) Emergency steering control of autonomous vehicle for collision avoidance and stabilisation, Vehicle System Dynamics, 57:8, 1163-1187, DOI: 10.1080/00423114.2018.1537494
-Use dynamic threat assessment model to evaluate risk associated with collision with surrounding actors based on road friction and the chosen vehicle configuration.
When a lane change is desired either to the right or left lane and possible in a safe way, the end point and maneuver time of the desired lane change maneuver are calculated
Modified Decision Making for lane change
Ego States
Actor States
Vehicle model & constraints
Road Condition(friction)
Control Actions

## Slide 5
Faults: We choose a few ASIL-D faults (like Tire pressure loss/impact of friction (snow conditions) and analyze which fault is crucial.
Ackermann steering fault.
Brake Sluggish response
Unintended acceleration/ loss of acceleration(lateral)
Tire blowout
We describe the redundancy needed for a road vehicle to meet certain safety goals.

## Slide 6: Ideas
Road adhesion coefficient as a function of vehicle velocity and thickness of water film
Safe longitudinal lane change distance based on conditions - optimization

## Slide 7
Models to start with:
Two-track dynamics with dug-off tire model
Powertrain: FWD single motor open differential (Including the entire drive shaft dynamics) (for chevy bolt)
TTC-based decision logic and quintic polynomial trajectory for a lane change in presence of dynamic actors
The influence of these parameters on the resulting autonomous vehicle control system and vehicle motion is important.
How well the chosen vehicle configuration ( with these uncertainties) performs the lane change in the presence of dynamic actors? (lane change feasibility). Also analyze the comfort for occupants in terms of parameters – ax, ay, and yaw acceleration.
Perform sensitivity analysis.
Recommend possible changes in the decision logic, and vehicle configuration(torque split, lateral dynamics) which can satisfy the uncertainties for a safe lane change.

## Slide 8: Parameters that are critical for lane changes during challenging weather conditions
Traction control
Reliable traction system requirement
Monitoring wheel slip and adjusting motor’s power output.
Vehicle Speed
Vehicle speed adjustment based on the road conditions
Steering and braking
Adjusting the steering and braking commands/ pressure to maintain control.
Road information
Access to updated road information to adjust its behavior to ensure a safe journey.
Vehicle Dynamics
Vehicle mass distribution
Tire road friction
Torque control for wheels
Sensor performance
Accurate detection in the presence of adverse weather conditions

## Slide 9
Highway Challenge for AutoDrive 2 requirements.
Vehicle needs to avoid the static obstacle ( road barricades) and change the lane.
Current plan:
Working on lane change algorithm for dynamic actors/ static actors.
Various lane change trajectories

## Slide 10
Three main categories in which path tracking algorithms can be classified: (1) Geometric path tracking methods; (2) Kinematic model-based path tracking methods; (3) Dynamic model-based path tracking methods
1) Geometric path tracking methods;
Based on the geometry of the vehicle and reference points.
2) Kinematic model-based path tracking methods;
By employing a kinematic model, all phenomena that occur between the wheels and the road, which give rise to the so-called slipping conditions, are neglected
3) Dynamic model-based path-tracking methods

## Slide 11: Highway Lane Change development framework
Sensor Fusion in Simulation
Reformat the sensor fusion data in a usable format.
Scenario and Sensor architecture design in MATLAB.
Develop lane change algorithm
Highway lane change for AutoDrive requires lane changing in the presence of a road barricade
(static obstacle and no moving vehicles)
Currently I am working on the model which can work for dynamic actors as well.
Lane change development process

## Slide 12: Developing lane change algorithm in the presence of dynamic actors.
Develop the lane change Algorithm
Interaction with other cars. (positions , velocities)
Take into consideration the uncertainty and unpredictability.
Safety parameters need to be considered
Lane change decision
Trajectory planning
Generate a trajectory that starts from the previous reference path and integrates into another lane
After changing the lane, another reference path has to be generated.
This process needs to be repeated whenever the vehicle performs the lane change and merges into another lane.
Reference points need to calculated in real time which is a challenge.

## Slide 13: Current Work:
Keep on calculating the real time reference points for the vehicle to follow according to
Follow lane
lane change left
lane change right
The existing controller models cannot handle the lane change maneuvers.
These maneuvers are high speed and have high lateral components of velocities and accelerations.
Develop a trajectory tracking controller which can handle the lane changes.
Trajectory generation and merging with previous path.

## Slide 14: Current software architecture
Scenario and sensor fusion models
Lane Change decision making model
Trajectory Generation
Dynamic model Stanley Controller
Single track 3 DOF bicycle model for vehicle Dynamics
Reference path generation in real time

## Slide 15: Effect of environment and vehicle uncertainties on lane change maneuver
What if there are uncertainties in the environment ( like adverse weather changes) and vehicle system
Vehicle mass distribution because of passengers.
Tire’s Cornering stiffnesses
Tire’s longitudinal stiffnesses
Environment effects
Vehicle system uncertainties
Impact of Rain/ snow on the road characteristics.
Adhesion Coefficient as a function of vehicle velocity and film thickness
Will the existing model still be able to perform effective lane change? Or will the vehicle start slipping? or any other effects?

## Slide 16
Realistic Road adhesion Coefficient
Vehicle mass distribution
Tire parameters
Cubic polynomial
Sigmoid based
Bezier curve based ( cubic, quintic)
Cosine function
Tangent hyperbolic
Determine the maximum lateral and longitudinal
accelerations and Jerks for each of these trajectories
Vehicle and Environment uncertainties
Parameter Combinations for sensitivity analysis
Parameter combinations for sensitivity analysis study on various trajectories
Evaluate performance metrics for each of these trajectories

## Slide 17: Vehicle Model and Dynamics
Ackermann steering
Two-track dynamics with dug-off tire model
Powertrain: FWD single motor open differential

## Slide 18
Part 1
Introduce these environment and vehicle uncertainties in the current model and analyze the performance on the output.
Understand which uncertainties affect the performance metrics for the lane change the most.
Perform the sensitivity analysis using cross array design of experiments approach.
Part 2
Design a multilevel adaptive lane change model that can take the uncertainties into picture.
(Minimum safe lane change distance based on road adhesion )
Develop an adaptive lane change system which consists of intelligent tracking
and control

## Slide 19
Lane-Change Model and Tracking Control for Autonomous Vehicles on Curved Highway Sections in Rainy Weather
Tao Peng,1,2Li-li Su,3Zhi-wei Guan,4Hai-jing Hou,1Jun-kai Li,5Xing-liang Liu,3and Yi-ke Tong6
Based on the scoring references under specific circumstances, a four-level lane-change mode for collision avoidance is proposed
Single track vehicle dynamics model
A scoring reference-based lane-change decision mechanism for collision avoidance on a curved road with low adhesion.

## Slide 20
Use of a configurable sigmoid function to generate a path to avoid the obstacle and the use of a rolling horizon to plan for a decomposed area of the path.
Each horizon is calculated and updated at each step
Pros: Reactivity to the obstacle motion and the generation of a smooth trajectory in a low execution time
W. Ben-Messaoud, M. Basset, J. -P. Lauffenburger and R. Orjuela, "Smooth Obstacle Avoidance Path Planning for Autonomous Vehicles," 2018 IEEE International Conference on Vehicular Electronics and Safety (ICVES), Madrid, Spain, 2018, pp. 1-6, doi: 10.1109/ICVES.2018.8519525.

## Slide 21
Lane Change Maneuver based on Bezier Curve providing Comfort Experience for Autonomous Vehicle Users
Il Bae1, Jin Hyo Kim2, Jaeyoung Moon1 and Shiho Kim1, Member, IEEE
Proposed an LCM algorithm based on evaluating the expected maximum lateral acceleration using the curvature of a Bezier curve and following the generated trajectory.
Used a desired lateral acceleration limit and compared it with bezer curvature limit
Used a linear bicycle model
No motor dynamics
No steer dynamics (Ackermann steering)
No variation in adhesion coefficients

## Slide 22
Lane-Changing Trajectory Tracking and Simulation of Autonomous Vehicles Based on Model Predictive Control
Hui Song , Dayi Qu *, Haibing Guo, Kekun Zhang and Tao Wang
MPC controller to track Quintic Bezier curve and validation for different road adhesions and vehicle speeds
Considered the ground adhesion (friction limits) for the
Acceleration constraints.
For different velocities, the MPC is able to handle the
Lane change with different friction coeff.
Focus on designing MPC controller with two track vehicle dynamics
With road friction friction constraints.

## Slide 23
"Sensitivity Analysis of Vehicle Parameters for Heading Angle Control of an Unmanned Ground Vehicle."
Sahoo, S, Subramanian, SC, & Srivastava, S. - Proceedings of the ASME 2014 International Mechanical Engineering Congress and Exposition.
A realistic mathematical model of the vehicle considering the steering actuator dynamics has been developed by calculating the cornering stiffnesses from the basic tire information and the vertical load on each tire.
Sensitivity analysis has been carried out to check the robustness and stability of the controller by varying the cornering stiffness of tires, the most uncertain parameter.
Varied the longitudinal speed and analyzed the heading angle change
At lower speeds, the controller is more sensitive to the steering actuator dynamics and at higher speeds, the controller is more sensitive to the cornering stiffness of tires

## Slide 24
Modelling the dynamic behavior of the steering system for low speed autonomous path tracking
Ádám Domina, Viktor Tihanyi
Considered the dynamic behavior of the steering system, including the effect of the tires.
The path following simulation with the improved model was calculated, which was compared to the real vehicle measurement and the results showed good correlation.
Comparision with three different tracking controllers

## Slide 25
Active Torque Vectoring in High Speed Lane Change Maneuvers." Steinbock, N, Prange, L, & Fabien, BC.
Proceedings of the ASME 2016 International Mechanical Engineering Congress and Exposition. Volume 4B: Dynamics,Vibration, and Control. Phoenix, Arizona, USA. November 11–17, 2016. V04BT05A034. ASME
We would like to increase the yaw and lateral accelerations that the vehicle can perform safely by controlling differing torques out of the two motors. Regulating these accelerations requires a control strategy over the left and right motor torques. Equal-torque control of the electric motors will be used as a baseline

## Slide 26: Lane Changes with safety
Commonly used collision avoidance methods:
Artificial Potential Field
Reachability analysis
Dynamic Window Approach
APF obstacle avoidance methods mainly rely on the repulsive force generated when approaching an obstacle to drive the robot away from the obstacle.
Target destination represents attractive force and obstalces represent repulsive
Easy to incorporate other effects as attractive/repulsive forces
APF methods are simple and efficient
Obstacle avoidance method based on the reachable set and also suitable for avoiding moving obstacles in a dynamic environment.
Reachable set represents the target set that robots can reach safely via control under any disturbance
The runtime computation is complex
Takes into account the dynamics and motion constraints of the robot.
Obtain samples in the speed space of the robot, predict its possible motion trajectory, and then use an objective function to evaluate the possible trajectory and achieve obstacle avoidance.
DYNAMIC AVOIDANCE RISK REGION
The collision risk region of a moving obstacle in a dynamic environment is located along its moving direction. The size of this region is closely related to the speed of the obstacle. High speed indicates a large risk region.

## Slide 27
B. Guo, N. Guo and Z. Cen, "Obstacle Avoidance With Dynamic Avoidance Risk Region for Mobile Robots in Dynamic Environments," in IEEE Robotics and Automation Letters, vol. 7, no. 3, pp. 5850-5857, July 2022, doi: 10.1109/LRA.2022.3161710.
First, using the state estimation of the extended kalman filter, a dynamic obstacle avoidance risk region is constructed along the direction of the obstacle movement.
Second, the robot’s safe obstacle avoidance operation against dynamic obstacles combined with nonlinear model predictive control is realized
The state estimation of the moving object combined with the equation of motion is recursively updated using the EKF algorithm
The collision avoidance mainly considers the states of the obstacles (future positions, direction, velocities)

## Slide 28: Artificial Potential Field Method

## Slide 29
Feng S, Qian Y, Wang Y. Collision avoidance method of autonomous vehicle based on improved artificial potential field algorithm.
Proceedings of the Institution of Mechanical Engineers, Part D: Journal of Automobile Engineering. 2021;235(14):3416-3430. doi:10.1177/09544070211014319
Designed an improved APF method for generating a safe and stable collision-free path in a dynamic traffic environment.
First, Influence range of obstacles is determined by the position, speed and direction, which is no longer a fixed value compared with a conventional algorithm.
Second, based on different obstacles (the threat level is determined by the mass, size and speed), the proposed position repulsion works to prevent collision accidents, and the defined speed repulsion decelerates the autonomous vehicle when necessary

## Slide 30
Wang P, Gao S, Li L, Sun B, Cheng S. Obstacle Avoidance Path Planning Design for Autonomous Driving Vehicles Based on an Improved Artificial Potential Field Algorithm. Energies. 2019; 12(12):2342.
Firstly, by analyzing the obstacle avoidance behavior of a human driver, a safety model of obstacle avoidance is constructed.
Then, based on the safety model, the artificial potential field method is improved, and the repulsive field range of obstacles are rebuilt
Safety Model of Obstacle Avoidance:
Obstacle avoidance model is constructed by combining the driving risk model and driver behavior characteristics

## Slide 31
Collision avoidance of 3-dimensional objects in dynamic environments
K Dhal, A Kashyap, A Chakravarthy - arXiv preprint arXiv:2203.09037, 2022 - arxiv.org
Modelled the shapes of the objects using suitable combinations of ellipsoids and one-sheeted/two-sheeted hyperboloids, and employ a collision cone approach to achieve collision avoidance.
This paper employs a collision cone based approach to de- termine collision avoidance laws for moving objects having elongated, non-convex shapes
The collision region is based on just the relative
Velocities of objects.
If the velocity vector of A lies inside the collision cone, then A is on a collision course with B, and needs to apply a suitable lateral acceleration aA to drive steer its velocity vector out of the collision cone.

## Slide 32
Model-Based Control of a Robotic Fish to Enable 3D Maneuvering Through a Moving Orifice
IEEE ROBOTICS AND AUTOMATION LETTERS, VOL. 5, NO. 3, JULY 2020
Given two moving objects A and B, A will pass through the orifice B, if the relative velocities belong to a specific set This set of relative velocities can be encapsulated
If the relative velocity vector does not lie inside this cone, then A needs to apply an appropriate acceleration a, that will steer the relative velocity vector into this cone, and this in turn will facilitate passage of A through B.

## Slide 33
An Improved Artificial Potential Field Model Considering Vehicle Velocity for Autonomous Driving
IFAC-PapersOnLine, Volume 51, Issue 31, 2018, Pages 863-867

## Slide 34
Yang, W.; Li, C.; Zhou, Y. A Path Planning Method for Autonomous Vehicles Based on Risk Assessment. World Electr. Veh. J. 2022, 13,234. https://doi.org/10.3390/ wevj13120234

## Slide 35
Predictive Collision Avoidance for the Dynamic Window Approach
2019 International Conference on Robotics and Automation (ICRA), Montreal, Canada, May 20-24, 2019
Change in the Dynamic Window Approach—a dynamic collision model—that is capable of predicting future collisions with the environment by also taking into account the motion of other objects
introduced a new version of predictive a DWA controller that explicitly models moving objects as polygons with velocities and computes future collisions.

## Slide 36
Y. Liu, X. Wang, L. Li, S. Cheng and Z. Chen, "A Novel Lane Change Decision-Making Model of Autonomous Vehicle Based on Support Vector Machine," in IEEE Access, vol. 7, pp. 26543-26550, 2019
Establishes an autonomous lane change decision-making model based on benefit, safety, and tolerance by analyzing the factors of the autonomous vehicle lane change.
Because of the multi-parameter and non-linearity of the autonomous lane change decision-making process, a support vector machine (SVM) algorithm with the Bayesian parameters optimization is adopted to solve this problem

## Slide 37
Z. -N. Li, X. -H. Huang, T. Mu and J. Wang, "Attention-Based Lane Change and Crash Risk Prediction Model in Highways," in IEEE Transactions on Intelligent Transportation Systems, vol. 23, no. 12, pp. 22909-22922, Dec. 2022, doi: 10.1109/TITS.2022.3193682.
An attention-based LSTM model is proposed in this paper for lane change behavior prediction in highways, considering both the surrounding vehicles’ information around the target vehicle at the current time and the historical trajectory data of the vehicle,
Pre-judgment model based on the C4.5 decision tree and bagging ensemble learning, and a multi-step lane change prediction model of LSTM with attention mechanism

## Slide 38
1) Ellipsoids can be fit relatively tightly to the profiles of vehicles, and 2) the sizes of both the ego vehicle and agent can be accounted for by properly scaling the size of the ellipsoid around the vehicle.

## Slide 39
Path Planning and Predictive Control of Autonomous Vehicles for Obstacle Avoidance
2022 18th IEEE/ASME International Conference on Mechatronic and Embedded Systems and Applications (MESA)